## Slide 1
Centralized Fleet Architecture: OPC UA PubSub over MQTT (DGX Spark gateway, Raspberry Pi fleet)
One OPC UA endpoint on the Spark models the whole fleet. Robots publish state and subscribe to commands over an MQTT broker, all within OPC UA.
OT platform
System services
MES and apps
Manufacturing exec
Cloud dashboards
Analytics
UaExpert
OPC UA browser
Single OPC UA endpoint opc.tcp port 4840 hosted on the DGX Spark, models the whole fleet (Arm1..ArmN)
DGX Spark | k3s server / edge gateway (role=edge)
OPC UA server
fleet address space, Arm1..ArmN
OPC UA PubSub
over MQTT
Edge AI inference
GPU, TensorRT
ROS 2 / OPC UA bridge
optional
MQTT broker OPC UA PubSub transport (over MQTT) robots publish state / subscribe to commands
Arm 1 (Pi, k3s agent)
PubSub client
pub state, sub cmd
ServoDriver + safe-stop
pigpio PWM, local
SG90 servos
base, pitch, reach, gripper
Arm 2 (Pi, k3s agent)
PubSub client
pub state, sub cmd
ServoDriver + safe-stop
pigpio PWM, local
SG90 servos
base, pitch, reach, gripper
Arm N (Pi, k3s agent)
PubSub client
pub state, sub cmd
ServoDriver + safe-stop
pigpio PWM, local
SG90 servos
base, pitch, reach, gripper
. . .
Key points
The Spark hosts one OPC UA endpoint; OT apps browse the whole fleet in a single session.
OPC UA PubSub over MQTT stays inside the OPC UA standard; the broker is its sanctioned transport.
Robots never host an inbound socket; each publishes its state and subscribes to its own command topic.
Safe-stop stays local on every Pi; k3s runs the control plane on the Spark and one agent per robot.