## Slide 1
Edge AI Robotics Architecture: OPC UA Backbone on k3s (Raspberry Pi + DGX Spark)
Robotic arm driven by a Raspberry Pi, exposed on the OPC UA backbone, with AI on the DGX Spark, all orchestrated by k3s.
OT platform
System services
MES and apps
Manufacturing exec
Cloud dashboards
Analytics
UaExpert
OPC UA browser
Secure backbone via OPC UA opc.tcp port 4840 certificate security (Basic256Sha256)
k3s cluster (one control plane, workloads pinned by node label)
DGX Spark | k3s server (role=edge)
OPC UA client
subscribes joint state
Edge AI inference
GPU, TensorRT
ROS 2 / OPC UA bridge
topic to node
OPC UA results server
publishes AI output (optional)
Raspberry Pi 5 | k3s agent (role=arm)
OPC UA arm server
asyncua, port 4840
ServoDriver
pigpio, DMA PWM
Safe-stop watchdog
local, network-independent
ROS 2 control node
joint commands
Robotic arm (OPC UA field device)
GPIO pins
BCM 13,12,18,19
External 5V PSU
common ground
SG90 servos
base, pitch, reach, gripper
Data flow and notes
Joint state flows up as setpoints; SG90 is open-loop (no encoder feedback)
Target commands flow down via the bridge and the arm server
Safe-stop runs locally on the Pi, independent of the network and Spark
Network: LAN, with an optional OT VLAN for segmentation